CN LAB-1
Disha Jain – 220905554 – B2

GNS3
1. Open terminal
2. $ python -m venv gns3env
3. $ source gns3env/bin/activate
4. $ pip install pyqt5
5. $ pip install gns3 - server
6. $ pip install gns3 – gui
7. $ gns3
Note: in subsequent labs only step 1,3 and 7 are required
Find the devices shown below from the left-hand side menu and create this network :

Click on and start all devices
Setting ip address and mask value of PC :
Right click on PC1 -> Console

- Similarly set up the rest of the Pcs.
- show ip command shows us all the details.

The ping command :
Syntax: ping [ip address to ping] (by default 5 packets sent)
When you want to specify number of packets :
Syntax: ping [ip address to ping] -c [no. of packets]

The save command :
Used to save the PC configurations so that we don’t have to re-enter next time
Wireshark:
- Used to visualise ping packets and do network monitoring
- Right click on any connecting medium -> Start Capture
- Observing wireshark for the same ping command as above

ARP – Address Resolution Protocol
ICMP – Internet Control Message Protocol

CISCO PACKET TRACER

Create a network as show below using tools available on bottom left corner

Sniffer here does the same job as Wireshark.

Setting ip address and mask value of PC :
Click on PC -> Desktop -> IP Configuration
The ping command :

- Click on PC -> Desktop -> Command Prompt
- Syntax: ping [ip address to ping]

To Connect Sniffer:
- Click on Sniffer -> GUI
- Observing the above ping